## Slide 1: Understanding and Creating Work Write-Ups and Requests for Bids
Contents
Quit

## Slide 2: Understanding and creating a Work Write-Up
This lesson will prepare you to:
Understand “Specifications” and Cost elements.
Understand the components of a viable Work Write-Up (WWU).
Create a WWU including cost estimates.
Contents
Quit

## Slide 3: Understanding and creating a Work Write-Up
Your CD contains the following:
A Specification Data Sheet
A blank Work Write-Up form
A blank Request for Bid form
Appendix A, “Trade ID” reference
Appendix B, “Unit of Measure” abbreviations
Written narrative and instructions
This tutorial
Contents
Quit

## Slide 4: Understanding and creating a Work Write-Up
Understanding and making sense of the
Specification Data Sheet. It contains:
Detailed instructions relevant to the specific task (column A)
Units of Measure (column C)
Unit Cost (column E)
Trade ID reference numbers (column (G)
Reference dates, titles, etc. (columns H&I)
Contents
Quit

## Slide 5: Understanding and creating a Work Write-Up
An example of the Specification Data Sheet layout is shown below
Contents
Quit

## Slide 6: Understanding and creating a Work Write-Up
Column A is titled “Specification”
Column A
Let’s examine each column individually
Contents
Quit

## Slide 7: Understanding and creating a Work Write-Up
A “Specification” is a description of exactly
What work will be performed.
The attributes of the material.
Description of how the material will be installed.
It may also specify specific brand names or describe unique circumstances.
Contents
Quit

## Slide 8: Understanding and creating a Work Write-Up
Column B
Column B is titled “Spec # ”
Contents
Quit

## Slide 9: Understanding and creating a Work Write-Up
The “Spec # ” is a number that identifies an individual specification along with other defining information.
Spec #’s are listed in ascending order with omissions in numerical sequences.
Contents
Quit

## Slide 10: Understanding and creating a Work Write-Up
Column C is titled “Unit (of) Measure”
Column C
Contents
Quit

## Slide 11: Understanding and creating a Work Write-Up
A “Unit of Measure” provides the customary common unit by which materials are normally sold. For example: flooring is sold by the “square yard”, molding by “linear foot”, concrete by the “cubic yard”, paint by the “gallon”.
Refer to Appendix B for the appropriate abbreviation for each unit of measure.
Contents
Quit

## Slide 12: Understanding and creating a Work Write-Up
Column D is titled
“Number of Units”
Column D
Contents
Quit

## Slide 13: Understanding and creating a Work Write-Up
“Number of Units” is the quantity of the Units (of) Measure required to perform the required task.
For example: paint is sold by the gallon, if 4 gallons of paint are required to paint the entire exterior, the number “4” would be entered here.
This is the only column where a value must be entered by the Rehab Specialist.
Contents
Quit

## Slide 14: Understanding and creating a Work Write-Up
Column E is titled
“Unit Cost”
Column E
Contents
Quit

## Slide 15: Understanding and creating a Work Write-Up
“Unit Cost” is the cost of each “Unit of Measure”
In our last example we needed 4 gallons of paint, the “Unit Cost” would be the cost of each gallon of paint.
Contents
Quit

## Slide 16: Understanding and creating a Work Write-Up
Column F does not have a title and is highlighted in orange. No data will be entered here.
Column F
Contents
Quit

## Slide 17: Understanding and creating a Work Write-Up
The purpose of column F is to serve as a buffer to remind the writer not to “copy” this column or anything to the right of this column when “pasting” information from the Specifications Data Sheet to the WWU.
Column F will have no information, values, or formulas entered into its cells.
Contents
Quit

## Slide 18: Understanding and creating a Work Write-Up
Column G is titled
“Trade ID”
Column G
Contents
Quit

## Slide 19: Understanding and creating a Work Write-Up
“Trade ID” is a number that is associated with an individual construction trade. (e.g. Carpentry has a Trade ID #10, Roofing has a Trade ID #11, Painting, #15). Note that under each trade, there are sub-sets of specialties: these are valuable when looking for a specific task.
Refer to “Appendix A” to associate each trade and their individual ID number.
Contents
Quit

## Slide 20: Understanding and creating a Work Write-Up
Column H is titled
“Mod Date”
Column H
Contents
Quit

## Slide 21: Understanding and creating a Work Write-Up
“Mod Date” is the date of the last modification to this Specification.
More importantly, it is the last date that a “Unit Cost ” sampling was done.
Contents
Quit

## Slide 22: Understanding and creating a Work Write-Up
Column I is titled “Spec Title”
Column I
Contents
Quit

## Slide 23: Understanding and creating a Work Write-Up
“ Spec Title” is the name of each individual Specification. It provides a very brief description of what is addressed in the Specification.
Contents
Quit

## Slide 24: Understanding and creating a Work Write-Up
OK, now let’s look at the “Work Write-Up” form. Notice that it contains information specific to the individual project:
Grant Recipient and the Grant number.
Home Owners Name, address, and phone number.
Inspectors name and the date of inspection.
Type of project (Rehab, Recon, Demo).
Some “Notes” and “Notices”.
Specifications Section.
Contents
Quit

## Slide 25: Understanding and creating a Work Write-Up
“Work Write-Up” continued,
Grant Info
Owner Info
Inspector Info
Notes & Notices
List of tasks specific
to rehab work
Contents
Quit

## Slide 26: Understanding and creating a Work Write-Up
Task # | SPECIFICATION | DCA Spec. # | Unit of Measure | No. of Units | Unit Cost | Line item Cost
1 |  |  |  |  |  | $ -
2 |  |  |  |  |  | $ -
3 |  |  |  |  |  | $ -
4 |  |  |  |  |  | $ -
5 |  |  |  |  |  | $ -
6 |  |  |  |  |  | $ -
7 |  |  |  |  |  | $ -
8 |  |  |  |  |  | $ -
Notice that the columns are arranged in the same order on both the Spec Data Sheet and the WWU sheet.
Contents
Quit

## Slide 27: Understanding and creating a Work Write-Up
Notice that columns “F” thru “I” do not appear on the WWU
Contents
Quit

## Slide 28: Understanding and creating a Work Write-Up
OK, now let’s create a Work Write-Up. NOTE: if you choose to actually perform each step as we move forward, minimize this ‘Power Point” presentation, return to the CD and open each form as indicated below. By alternately minimizing and restoring each screen, you can create an actual WWU.
Step 1: Gather all notes, drawings, measurements, and photos.
Step 2: Open the blank “Cost Estimate Work Write-Up” form.
Step 3: Do “Save As” and name it the what ever you like – the home owners name would make sense.
Step 4: Fill in all the information requested in the Grant Info, Owner Info, Inspector Info sections.
Step 5: Open the “Specification Spec Data Sheet”
Step 6: Now we’re ready to “copy” data from the Specifications Data Sheet and “paste” into the Work Write-Up form.
Contents
Quit

## Slide 29: Understanding and creating a Work Write-Up
Your notes indicate that the 4” baseboard molding in bedroom #1 needs replacing. The room measures 10’ x 15’ with a 3’ door opening.
Refer to “Appendix A”, scroll down the “Trade Sub-Specialty” column and find “Molding and Trim” listed under the Carpentry Trade ID: #10
Now refer to the “Specifications Data Sheet”, scroll down column “G”: Trade ID, until you come that section listing #10 in the column.
Refer to the column immediately to its right, column “I”: “Spec Title”, scroll down thru the column until you come to the “floor molding” section and find a title pertaining to “Baseboard…1x4”, it so happens to be “Spec” #2410.
Contents
Quit

## Slide 30: Understanding and creating a Work Write-Up
Specification | DCA Spec # | Unit Measure | No. of Unit | Unit Cost |  | 10 | Feb-98 | 
 |  |  |  |  |  | 10 | Feb-98 | **FLOOR MOLDING**
Install finger jointed 9/16" x 3-1/2" ranch base with finish nails or tee headed brads. | 2405 | LF |  | $2.45 |  | 10 | Feb-98 | BASEBOARD--RANCH
Install 1"x4", #2 grade pine base with finish nails or tee headed brads. | 2410 | LF |  | $2.10 |  | 10 | Feb-98 | BASEBOARD--1"X4"
Install pine shoe molding nailed 2' on center to create the tightest possible seal between the baseboard and floor using finish nails or tee headed brads. | 2415 | LF |  | $0.87 |  | 10 | Feb-98 | SHOE MOLDING
Install base cap on 3-piece baseboard assembly to match original as closely as possible. | 2420 | LF |  | $0.81 |  | 10 | Feb-98 | BASEBOARD TOP
Locate Spec #2410.
Now highlight ONLY columns “Specification” thru
“Unit Cost”.
From the “edit tool bar, select “Copy” to copy these 5 cells highlighted in yellow.
Contents
Quit

## Slide 31: Understanding and creating a Work Write-Up
Open the WWU for the project.
Type the location of the task in the blank row above “Task# 1: in this case Bedroom #1
Now go to Task #1 and highlight ONLY cell “B”, “Specification”. From the “edit” tool bar press “paste”.
Contents
Quit

## Slide 32: Understanding and creating a Work Write-Up
Our bedroom measured 10’x15’ with a 3’ door. That comes to a total of 47’. Highlight cell “D” and enter “47 ”.
“Excel” will multiply the “No. of Units”, 47 times the “Unit Cost”, $2.10 per linear foot and enter the product into the “Line Item Cost” cell.
It will probably be necessary to add additional rows as you add additional task,
simply “insert” a new row; be sure to copy the formula contained in the
“Line Item Cost” cell and paste into you’re your new row.
Contents
Quit

## Slide 33: Understanding and creating a Work Write-Up
Repeat this “copy” and “paste” process until all individual tasks have been entered into the WWU.
As you enter each task, “Excel” will keep a running total of each “Line Item Cost” at the bottom.
You may choose to add in a Profit & Overhead margin.
At the completion of the WWU, have the home owner sign and date the document.
Contents
Quit

## Slide 34: Understanding and creating a Work Write-Up
Your finished document should look something like this.
Grant and Owner
information
Tasks Write-Ups
Costs and totals
Contents
Quit

## Slide 35: Understanding and creating a Work Write-Up CONCLUSION
Points to remember:
Have all materials (notes, measurements, drawings, etc.) on hand before you begin a WWU.
Complete all Grant and Homeowner information.
Refer to the Specification Data Sheet and select the most appropriate task specification possible; modify if necessary.
Attempt to ensure the “Unit Cost” data is a current as possible.
Have the Homeowner sign and date the WWU.
Do not release the WWU info to anyone.
Contents
Quit

## Slide 36: Understanding and creating a Work Write-Up
Congratulations:
you have successfully completed a complete and viable Work Write-Up.
Now, let’s do the corresponding “Request For Bid”.
Contents
Quit

## Slide 37: Understanding and Creating a “Request For Bid”
Contents
Quit

## Slide 38: Understanding and creating a Request For Bid
This lesson will prepare you to:
Create a “Request For Bid” (RFB) based on the Work Write-Up you just completed.
Defines exact Scope of Work on which the contractor will bid.
Evaluate the reasonableness of the submitted bids.
Negotiate with realistic cost estimates.
Contents
Quit

## Slide 39: Understanding and creating a Request For Bid
Notice that the columns in the Request for Bid are arranged in the same order as they were on the Spec Data Sheet and the WWU sheet.
Contents
Quit

## Slide 40: Understanding and creating a Request For Bid
OK, now let’s look at the “Request for Bid” form. Notice that it contains the same information, in the same order as did the WWU:
Grant Recipient section, Homeowners section, project type, “Notices”, specifications and spec #, unit of measure, number of units, unit cost, and line item cost.
What cells are not filled-in on the RFB:
Unit Cost (value)
Line Item Cost (value)
Sub-total (value)
P&O percentage (value)
Contents
Quit

## Slide 41: Understanding and creating a Request For Bid
Because the WWU and the RFB formats are basically identical: you can create a RFB simply by:
“Copy” and “Paste” information from the WWU cells into the RFB cells.
Contents
Quit

## Slide 42: Understanding and creating a Request for Bid
Your finished document should look something like this.
Owner information
Tasks Write-Ups
NO Unit Cost or
Line Item Cost
Contents
Quit

## Slide 43: Understanding and creating a Request for Bid CONCLUSION
Points to remember:
All information presented on the RFB originated on the WWU.
When completing a RFB, always be certain that the “Unit Cost – column E” and “Line Item Cost – column G” cells are blank.
Contents
Quit

## Slide 44: Understanding and creating a Request for Bid
We hope that this program and tutorial will enable you to create solid Work Write-Up and Request for Bid forms with no “wiggle room” for misunderstandings or conflicts.
We, at DCA, encourage you to provide feedback as the usefulness, practically, corrections, and welcome any other comments as you so desire.
Technical support and other questions may be obtained by contacting:
Thomas Spinks
Sr. Housing Consultant
Georgia Department of Community Affairs
60 Executive Park South, N.E.
Atlanta, Georgia 30329
(404) 679-3128
tspinks@dca.state.ga.us
Quit